## Slide 1: Intro to DSP Filters
June 2020

## Slide 2
Rules of thumb, assumptions and mixed-quality analogies to come!

## Slide 3: What is a DSP Filter?
DSP = Digital Signal Processing
Fancy
Microprocessor
Input
Output
Input
Output
≠ Analog Signal Processing

## Slide 4: Audio Implementation
Fancy
Microprocessor
ADC
DAC

## Slide 5: Why use Analog vs Digital Processing?
Analog:
Infinite bandwidth
  Good for high frequency applications
Doesn’t require ADC, microprocessor
Can offload complexity from processor
Digital:
Can change filter characteristics easily
More ideal filters are possible
Can do types of processing that analog can’t
  Data compression
  Math operations like cos(), atan()
  Pattern recognition, red-eye reduction
Lots of specific knowledge (Nyquist sample rates, quantization noise, etc.)

## Slide 6: Where is DSP Used
Radars
Sonars
Speech Recognition
Image Processing
Channel Equalization
Medical Imaging
Speaker Crossovers
Mobile Phones (Speech Coding, Noise Reduction)

## Slide 7: Ex: Radar Pulse Compression[1]
Radar: emits a pulse of a specific shape and looks for a reflected pulse that matches that shape

## Slide 8: Ex: Radar Pulse Compression[2]
“Matching Filter”:
Looks for correlation between received signals and the emitted pulse
Received Signal
Post-Processed Signal

## Slide 9: Ex: Parametric EQ [3]
DSP equalizer can allow the user to tailor frequency response nearly infinitely

## Slide 10: How are DSP filters implemented?
x[0] | x[1] | x[2] | x[3] | x[4] | x[5] | x[6] | x[7] | x[8] | x[9]
w[0] | w[1] | w[2]
* * *
y[0]
y[0]= x[0]*w[0] + x[1]*w[1] + x[2]*w[2]

## Slide 11: How are DSP filters implemented?
x[0] | x[1] | x[2] | x[3] | x[4] | x[5] | x[6] | x[7] | x[8] | x[9]
w[0] | w[1] | w[2]
* * *
y[0] | y[1]

## Slide 12: How are DSP filters implemented?
x[0] | x[1] | x[2] | x[3] | x[4] | x[5] | x[6] | x[7] | x[8] | x[9]
w[0] | w[1] | w[2]
* * *
y[0] | y[1] | y[2]

## Slide 13: How are DSP filters implemented?
x[0] | x[1] | x[2] | x[3] | x[4] | x[5] | x[6] | x[7] | x[8] | x[9]
w[0] | w[1] | w[2]
* * *
y[0] | y[1] | y[2] | y[3] | y[4] | y[5] | y[6] | y[7]
This is called “Convolution”

## Slide 14: 2D Convoluton Example[4][5]

## Slide 15: DSP Filter Block Diagram
Input
Signal
Summer
x1.0
X0.5
Delay 1 Sample
Output
Signal
Xt
Xt-1
X

## Slide 16: DSP Example
Summer
x0.5
X0.5
Delay
Output
Signal
Time | Value
1 | 0
2 | 1
3 | 1
4 | 0
5 | 0
6 | 0
… | …
0
0
0
0
0+0=0
t=1
0
Time | Value
1 | 0
2 | 
3 | 
4 | 
5 | 
6 | 
… | …

## Slide 17: DSP Example
Summer
x0.5
X0.5
Delay
Output
Signal
Time | Value
1 | 0
2 | 1
3 | 1
4 | 0
5 | 0
6 | 0
… | …
1
0
0.5
0
0.5+0=0.5
t=2
0.5
Time | Value
1 | 0
2 | 0.5
3 | 
4 | 
5 | 
6 | 
… | …

## Slide 18: DSP Example
Summer
x0.5
X0.5
Delay
Output
Signal
Time | Value
1 | 0
2 | 1
3 | 1
4 | 0
5 | 0
6 | 0
… | …
1
1
0.5
0.5
0.5+0.5=1
t=3
1
Time | Value
1 | 0
2 | 0.5
3 | 1
4 | 
5 | 
6 | 
… | …

## Slide 19: DSP Example
Summer
x0.5
X0.5
Delay
Output
Signal
Time | Value
1 | 0
2 | 1
3 | 1
4 | 0
5 | 0
6 | 0
… | …
0
1
0
0.5
0+0.5=0.5
t=4
0.5
Time | Value
1 | 0
2 | 0.5
3 | 1
4 | 0.5
5 | 
6 | 
… | …

## Slide 20: DSP Example
Summer
x0.5
X0.5
Delay
Output
Signal
Time | Value
1 | 0
2 | 1
3 | 1
4 | 0
5 | 0
6 | 0
… | …
0
0
0
0
0+0=0
t=5
0
Time | Value
1 | 0
2 | 0.5
3 | 1
4 | 0.5
5 | 0
6 | 
… | …

## Slide 21: DSP Example
Summer
x0.5
X0.5
Delay
Output
Signal
Time | Value
1 | 0
2 | 1
3 | 1
4 | 0
5 | 0
6 | 0
… | …
0
0
0
0
0+0=0
t=5
0
Time | Value
1 | 0
2 | 0.5
3 | 1
4 | 0.5
5 | 0
6 | 0
… | …

## Slide 22: DSP Example Result

## Slide 23: Fancy Maths – Please Ignore!
H(z) =
H(z) =
H() =
H() =
H() =
=
=
= τ g, τ=
Frequency
Domain
Response
Phase Response
Group Delay Response

## Slide 24: Frequency Response Plot
=
Input
∑
X0.5
X0.5
T
Output

## Slide 25: Normalized Frequency
π = Nyquist Frequency
= ½ Sample Rate
If we sampled at 10kHz
Then π = 5kHz

## Slide 26: Practical – Use Calculator[6]
Set filter properties

## Slide 27: Practical – Use Calculator[6]
Get block diagram

## Slide 28: Practical – Use Calculator[6]
Copy generated code

## Slide 29: DSP Microprocessors[7] Fast Multiply-Accumulate
Oriented towards fast execution of multiply/add of a series of filter coefficients and sample data points
SHARC DSP:
One clock cycle: multiply, add, 2 data moves, update 2 circular buffer pointers, loop control
A 100 tap FIR filter is executed in 105-110 cycles
Traditional CPU, several thousand cycles

## Slide 30: DSP Microprocessors[7] Circular Buffers
Circular Buffer
Holds sampled data
New data point rolls in
Oldest point rolls out
Extremely fast updates
Address | Sample Value | Time
10000 | 0.0544 | x[n-4]
10001 | 0.1827 | x[n-3]
10002 | 0.3488 | x[n-2]
10003 | 0.8447 | x[n-1]
10004 | 0.3712 | x[n]
10005 | 0.3947 | x[n-7]
10006 | 0.7640 | x[n-6]
10007 | 0.6671 | x[n-5]
Newest
Oldest
V

## Slide 31: DSP Microprocessors[7] Extended Precision Accumulator
Typical 16 processor -> 16 bit accumulator
A 10 tap filter means 10 adds. To prevent overflow we scale the numbers by 1/10.
Now the signal strength has been reduced by 90%
Worsens signal to noise ratio dramatically for filters with large operations
A DSP processor would have a 32 – 40 bit accumulator

## Slide 32: DSP Microprocessors Floating vs Fixed Point
Fixed -> cheaper
Floating -> better and easier
ADSP-21161: Ways to multiply 2 numbers
Fixed
Float

## Slide 33: Guitar Effects Processor
Strymon BigSky effects processor - Analog Devices SHARC running at 366MHz
Samples at 96,000 samples/second
3,800 operations per sample (e.g. multiple/add)

## Slide 34: Artificial Reverb[8]
Typically use “Schroeder Allpass Sections”
g is less than 1 (typically ~0.7)

## Slide 35: Computational Loads[9]
5G Application:
CEVA-XC Gen 4: 1.8GHz, 7nm, 1.6 teraflops/sec
Audio: hi-fidelity, looking for 44kHz:

## Slide 36: References
[1] https://www.intechopen.com/books/radar-technology/radar-performance-of-ultra-wideband-waveforms
[2] https://en.wikipedia.org/wiki/Pulse_compression
[3] http://help.izotope.com/docs/rx/pages/reference_parametricequalizer.htm
[4] https://leonardoaraujosantos.gitbooks.io/artificial-inteligence/content/convolution.html
[5] https://medium.com/@james.chain1990/study-3d-convolutional-neural-networks-for-human-action-recognition-7eaeb9a0ec00
[6] https://www.micromodeler.com/dsp/
[7] http://www.dspguide.com/ch28/3.htm
[8] https://ccrma.stanford.edu/~jos/pasp/Schroeder_Allpass_Sections.html
[9] http://openaudio.blogspot.com/2016/10/benchmarking-teensy-36-is-fast.html