## Slide 1: Intro to Electronics
Mar-2019

## Slide 2
Rules of thumb, assumptions and mixed-quality analogies to come!

## Slide 3: Plumbing Analogy

## Slide 4: Powering a Light Bulb
Voltage is the pressure (pushing force)
Pushes electrons through a circuit

## Slide 5: Voltage
+
1.5V
-
+
1.5V
-
+
1.5V
-
+
1.5V
-

## Slide 6: Powering a Complex Circuit
Voltage is applied across any circuit to power it
12V

## Slide 7: Measuring Voltage
Voltage is measured between/across two points:
  Positive minus negative
  Convention - red minus black

## Slide 8: Common Voltages
110 volts AC
110V or 110V AC or
110VAC
Volts DC:
9V or 9VDC or 9V DC
12V DC or
12V

## Slide 9: Let’s Try It!
5V DC
2.5V DC
Jumper
Ground

## Slide 10: Current
Current is the flow of electrons
Similar to the flow of water

## Slide 11: Current
Measured in amps
1A (1 amp) = 6.25 x 1018 electrons per second

## Slide 12: Measuring Current
Current can be measured by passing it through a multimeter

## Slide 13: Let’s Try It!
~0.5mA DC
Remove Jumper

## Slide 14: “Voltage Across” – “Current Through”
Voltage
Current

## Slide 15: Power
Power = Watts = Amount of energy used at a particular point in time
Energy =
Power x Time = W x hr
Total energy used over a period of time

## Slide 16: Calculating Power
Power = Voltage x Current
120V x 0.5A = 60W

## Slide 17: Resistors – A minute to learn, a lifetime to master

## Slide 18: We use them every day

## Slide 19: Resistors – Resist the flow of current
Resistance – measured in Ohms (Ω)

## Slide 20: Conductors vs Insulators

## Slide 21: All Shapes and Sizes

## Slide 22: Fixed Resistors – Construction

## Slide 23: Variable Resistors – Construction

## Slide 24: Resistors – Simple but useful!

## Slide 25: Ohm’s Law
Special Relationship between voltage, current, resistance
V = I * R

## Slide 26: Ohm’s Law
V = I * R
R = V / I
I = V / R
120V
I=0.5A
I=?
R=?

## Slide 27: Let’s Try It!
R = 4.7kΩ
V = I * R
R = V / I
I = V / R
Remove jumper, measure R
V = 2.5V
Place jumper, measure V
V = 0.53mA
Remove jumper, measure I

## Slide 28: Resistors in Series
R1 + R2 + R3 + R4
=
10Ω
10Ω
10Ω
10Ω
40Ω

## Slide 29: Resistors in Parallel
=
RT
10Ω
40Ω
40Ω
40Ω
40Ω
RT =
1
+
+
+
1
R1
1
R2
1
R3
1
R4

## Slide 30: Let’s Try It!
R1 = R2 = 10kΩ
Remove jumpers, measure each R
R3//R5 = 5kΩ
R3 = R5 = 10kΩ
10kΩ
10kΩ
5kΩ

## Slide 31: Diodes/LEDs

## Slide 32: Diodes – Everyday Uses

## Slide 33: Diodes – One-Way Gate
Current Flow
LED

## Slide 34: How to use a diode
VS > VLED + 1V
ILED ~ 10-20mA
VLED ~ 1.8-3.3V
+
VS
VLED
R
ILED
+
-
-

## Slide 35: Practical Circuit
R = (5V – 2V) / 0.01A
= 3V / 0.01A
= 300Ω
+
VS = 5V
VLED = 2V
R = ?
I = 10mA
R = V / I
+
-
-

## Slide 36: Let’s Try It!
V = I * R
R = V / I
I = V / R
V = 2.5V
Place jumper, measure V
R = 100Ω
Remove jumper, measure R
V = 0.53mA
Remove jumper, measure I
Turn knob to set brightness

## Slide 37: Switches

## Slide 38: Capacitors

## Slide 39: Similar to Batteries

## Slide 40: “Supply Bypass” Capacitors

## Slide 41: Further Reading
Falstad Circuit Simulator – Runs in Browser
Kahn Academy – Introduction to EE
Mattermost Channel
YouTube Videos
All About Circuits
https://www.allaboutcircuits.com/education/
Sparkfun – learn.sparkfun.com