## Slide 1: Analog Circuits 101
Dec 2018

## Slide 2
Rules of thumb, assumptions and mixed-quality analogies to come!

## Slide 3: Digital Signals
Discrete in time and amplitude (voltage)
Convey a series of symbols (e.g. 0, 1, 1, 0, 1, 0, 0, 0, 1, 0)
Low information density but relatively immune to noise

## Slide 4: Digital Signals
Voltage levels don’t need to be precise
Wide ranges of circuits can just plug together

## Slide 5: Digital Signal Examples

## Slide 6: Digital Signal Integrity Issues
Preserve adequate rise/fall times
Keep ringing under control

## Slide 7: Analog Signals
Continuous in time and voltage (amplitude)
Represent some time varying quantity (e.g. sound pressure)
Potentially infinite information density (theoretically)

## Slide 8: AC vs DC Components
AC
DC

## Slide 9: Analog Signal Characteristics
Linear or nonlinear
Can be distorted
Maybe small voltage levels
Can be noisy
Welcome to the real world!

## Slide 10: Example: Simple Motor Control
Analog voltage to be converted to digital by Arduino
Knob

## Slide 11: Example: Audio Amplifier
Increase signal amplitude
Input signal has +/- voltage, no DC
Output has +/- voltage, no DC
Not too much distortion

## Slide 12: Example Signal - ECG
Non-invasive
12 leads on body
Measures electrical changes on the skin due to heart activity
<1mV signal
  Fetal ECG ~1µV
10kHz bandwidth

## Slide 13: What makes analog hard?
Digital – thinking process is more like a logic puzzle; circuit elements are often fairly ideal building blocks
Analog –uses non-ideal components and “true” circuit design principles
  Signal min/max voltages
  DC offsets
  Distortion
  Bandwidth

## Slide 14: Project Time!
Let’s amplify a signal so it can optimally feed a microcontroller ADC

## Slide 15: Signal Observations
+/- 0.45V
(0.9VP-P)
0 - 5.0V (5VP-P)
5V Supply
Both +/- voltages
DC = 0V
<20KHz
Only + voltage
DC = 2.5V
<20KHz
Amplify x5.5
Add 2.5V DC

## Slide 16: Let’s introduce the op-amp!
V-
-
+
VOUT
V+
Will set VOUT to force V- = V+
stuff
stuff
VIN

## Slide 17: Ideal op-amp
V-
-
+
VOUT
V+
Ideal Op-Amp: Current into V+, V- is zero
V+ = V- (in “closed loop” operation)
Infinite “open-loop” gain: VOUT = (V+ - V-) x ∞
Paraphrase: It’s really good at trying to set VOUT to force V- = V+

## Slide 18: Open Loop Systems
A system that does its thing without measuring what’s happening

## Slide 19: Closed Loop Systems
A system that adapts what it’s doing based on what’s happening

## Slide 20: Closed Loop Systems
feedback
Valve
Flow Meter
Controller

## Slide 21: Standard Inverting Amplifier
Ideal Op-Amp: Current into V+, V- is zero
V+ = V- (in closed loop circuit)
Infinite open-loop gain
VOUT
Rf = 20kΩ
Ri = 10kΩ
VIN
-
+
V-
V+
VOUT = -VIN x (Rf/Ri)

## Slide 22: Real op-amps: VIN Limits
MCP6002
LM741
VOUT
VIN
-
+
“rail-to-rail” input
not “rail-to-rail”

## Slide 23: Real op-amps: VOUT Limits
VOUT
VIN
-
+
MCP6002
LM741
“rail-to-rail” output
not “rail-to-rail”

## Slide 24: Input/Output DC Voltage Problem
VIN has no DC component (it’s an AC signal centered around 0V DC)
VOUT should vary from 0V to 5V (centered around 2.5V DC)
5V
0V
0.45V
-0.45V
VOUT
VIN
-
+

## Slide 25: Real op-amps: I/O DC Offsets
VOUT
100k
VIN
-
+
+5V
DC = 0V
AC = +/-0.45V
DC = 2.5V
AC = +/-2.5V
100k
+5V
45K
10K
C2
C1
DC = 2.5V
AC = +/-0.45V

## Slide 26: Final Circuit
VOUT
100k
VIN
-
+
+5V
DC = 0V
AC = +/-0.45V
DC = 2.5V
AC = +/-2.5V
100k
+5V
45K
10K
1uF
1uF
1uF
1uF
100k
100k

## Slide 27: Making op-amp circuits easier
Become familiar with a few basic op-amp circuits
Inverting amp
Non-inverting amp
Summing amp
Take advantage of proven designs:
application notes
examples in data sheets, websites
op-amp cookbooks
Go-to parts:
Have a go-to rail/rail I/O 5V op-amp (KM MCP6002)
Have a go-to split-supply 30V op-amp (KM NE5534)
Unity gain stable, GBW ~MHz

## Slide 28: Finished Circuit

## Slide 29: Using a breadboard
Power supply buses
Circuit connections
Internals of board

## Slide 30: Using a Multimeter
Voltage across
Current through
Resistance between
Continuity between