## Slide 1: Power Supplies 101 DC-DC Converters
10-Feb-2018

## Slide 2: Tonight’s Agenda
Quick primer on circuit components and basic calculations
Examples of unregulated linear supplies
How regulated linear supplies work
How switching supplies work
Some notes on capacitors
Cover related issues that you’re likely to encounter

## Slide 3: Quick circuit component primer
Wire – carries electrical current like a pipe carries water
Voltage – like the pressure of water in a pipe or air in a tire
Current – the amount of water flowing through a specific cross section of the pipe
Resistor – resists the flow of current, like a constriction in a pipe
Capacitor – stores energy like a hydraulic accumulator
Inductor – stores energy like a heavy paddlewheel

## Slide 4: Power supply math primer
Ohm’s Law:
V = I x R
or: I = V / R
or: R = V / I
V = voltage, volts, V
I = current, amps, A
R = resistance, Ohms, Ω
Units:
1000 milli = 1.0
400mA = 0.4A
10mV = 0.01V
2000 mΩ = 2Ω
Power (P, watts, W) = Voltage (volts, V) x Current (amps, A)
Power = 5V x 2A = 10W

## Slide 5: Examples
What is the power rating of a 5V, 2A power supply?
Power = Voltage x Current
5V x 2A = 10W
How much current does a 60W light bulb draw?
Current = Power / Voltage
60W / 120V = 0.5A
A 100Ω resistor is connected between a 12V supply and ground, how much current does it draw?
I = V / R
= 12V / 100Ω = 0.12A = 120mA
How much power does it dissipate?
Power = Voltage x Current
= 12V x 120mA = 1.44W
5V @ 2A
Power?
12V
I?
120V
I?
60W bulb

## Slide 6: Simple Voltage Converter/Supply
12V
IBIAS
VOUT = R2/(R1+R2)
R1
R2
ILOAD
Example: 12V to 5V, 10mA load
R1 = 70Ω
R2 = 50Ω
IBIAS = 100mA
VOUT, NO LOAD = 5.0V
VOUT, 10mA LOAD = 4.7V
Load regulation = 6%
Efficiency = 9.6%

## Slide 7: Zener Voltage Reference/Supply
12V
IBIAS
VOUT=VZENER
R1
ILOAD
Decent load regulation ~2-5%
Efficiency ~30%

## Slide 8: More unregulated supplies

## Slide 9: How does a linear regulator work?
VIN
Resistor converts extra voltage into heat
VOUT will be less than VIN
Efficiency = VOUT/VIN
5V / 12V = 42%
3.3V / 5V = 66%
VOUT
e.g. 12V
e.g. 5V

## Slide 10: Add a control loop
VIN
VOUT
Reference
Voltage
Stuff

## Slide 11: Make it more real
VIN
VOUT
1.2V
Reference
-
+

## Slide 12: Linear regulator in action
https://www.diodes.com/assets/Datasheets/AP1117.pdf

## Slide 13: Power Supply Rejection
https://e2e.ti.com/blogs_/b/powerhouse/archive/2017/03/03/ldo-basics-power-supply-rejection-ratio
20dB = 1/10
40dB = 1/100
60dB = 1/1000
70dB = 1/3162 -> Vin ripple of 1V results in 0.3mV at Vout

## Slide 14: Typical Hardware
$1.70
$1.60
$1.50
$0.99
$0.50-$1.00
$0.50
$0.05
$1.00
@mikew

## Slide 15: Workhorse linear regulators ICs
 | VIN Max | VOUT Range | VDO Dropout | Peak IOUT
LM317 | VOUT + 40V | 1.25V to 37V | 3V | 1.5A
LM1117 | 15V | 1.25V to 13.8V | 1.3V | 1A
LM7812 | 35V | 12.0V | 2V | 2.2A
LM7805 | 35V | 5.0V | 2V | 2.4A
LM7833 | 36V | 3.3V | 2V | 1.8A
These regulators are available from multiple manufacturers. Check the data sheet for the specific part you’re looking at.

## Slide 16: DC-DC Switching Supplies
Buck converter: VOUT < VIN
  Very plentiful selection of products
Boost converter: VOUT > VIN
  Inductor-less Charge Pump, typically 10’s of mA
  Inductor based boost converter, any current
Buck/Boost converter: VOUT >= or <= VIN
  Useful in battery powered circuits where the battery voltage starts above the required voltage but ends below it
    e.g. LED flashlight

## Slide 17: How does a buck regulator work?
VOUT = VIN x DutyCycle
VIN
Filter
VOUT
V
time
V
time
5V
12V
DutyCycle = ton/T

## Slide 18: Add a control loop (regulation)
VIN
Filter
VOUT
Reference
Voltage
Clock/
Logic/
Stuff

## Slide 19: Make it more real
Could be a FET
Quality of TR1, D1 and L1 affect Efficiency
Filter

## Slide 20: Buck, Boost, Buck/Boost
Slight modifications in the schematic, operation is quite different from the earlier buck explanation

## Slide 21: Flyback Converter
Transformer is used in place of an inductor
One or many outputs
Feedback loop (regulation) based on one output or some weighted average of multiple outputs

## Slide 22
Agilent Bench Supply

## Slide 23: DC-DC linear vs switching supplies
 | Pros/Cons
Switching (Regulated) | Easy to buy/use Typically preferred over ~1A of output current Typically overly-complicated for low power circuits (100’s of mW)
Linear Regulators | Easy to build, easy to buy Easy to integrate onto proto boards Becomes more difficult as PDISS increases beyond a few watts Off-the-shelf options above 1A are limited

## Slide 24: About Capacitors
Capacitance value
Physical size
Lead configuration (axial, radial)
Voltage rating
Polarized
Equivalent Series Resistance (ESR)
Equivalent Series Inductance (ESL)
Appropriate frequency range

## Slide 25: Electrolytic Capacitors
Electrolytic (Aluminum)
Primarily used for bulk capacitance, up to 10,000’s of µF
Lots of disadvantages:
  Polarized (typically)
  Need to check voltage rating, derate 20%
  Physically large
  High equivalent series resistance
  High equivalent series inductance
  Doesn’t look like a capacitor much above 100kHz
Electrolytic (solid tantalum)
Similar to aluminum electrolytic except:
  Smaller
  Better (lower) ESR, ESL
  Frequency response to ~500kHz, maybe 1MHz
Derate voltage by 50%
Overvoltage or wrong polarity can cause a fire

## Slide 26: Ceramic Capacitors
Film
Often thought of as an alternative to ceramics for audio
Benefits:
  Linear response
  No microphonics
  Slightly higher capacitance than ceramics
  Good heat and vibration tolerance

## Slide 27: Film Capacitors
Ceramic
Looks the most like an ideal capacitor
Low capacitance value (1uF is a large ceramic cap)
Not polarized
High voltage ratings (typ 100V)
Very low equivalent series resistance
Very low equivalent series inductance
Frequency range, 10’s or 100’s of MHz
Capacitance is highly voltage dependent
  ~80% lower at rated voltage
  Due to ferroelectric dipoles
  Nonlinearity makes them less desirable in hifi audio
Piezoelectric

## Slide 28: Bypass caps, rules of thumb
Where to put them
Where power enters a board
Near the VCC pin of each IC
Input and output of linear regulator ICs
Values and types:
0.1uF ceramic is the workhorse for typical digital/analog
Maybe add a 10µF or so where power enters the board
AC rectifier circuits tend to use 1000’s of uF
Larger bypass caps are needed with:
Larger current swings
Lower frequency
Power supply feed lengths get longer
Star feed is better than daisy chain feed
Typical low current circuits -> 0.1uF ceramic cap every several inches

## Slide 29: Measuring Current Draw of a Circuit
ILOAD = VDROP / RSENSE
+
VSUPPLY
Load
RSENSE
+ VDROP -
ILOAD
VDROP should be large enough for a multimeter to measure it accurately but not so large that it affects the circuit being powered
  0.1V < VDROP < VSUPPLY / 10
1/8W
1/4W
1/2W
1W
2W
3W
5W
Check that resistor is rated for dissipated power
If it’s too hot to touch, measure fast
PDISS = VDROP x ILOAD

## Slide 30: Determining if you’ll run too hot
Build it, feel the device, if it’s too hot to touch for 0.5 seconds, add a heat sink, choose a larger regulator or do something else about it
Or, rules of thumb->

## Slide 31: Thermal Rules of thumb based on packaging
Package | RJA | Max Power No Heat Sink | Accommodates Heat Sink? | Picture
TO-220 | ~20 | ~2-4W | Yes | 
DDPAK | 44 | ~1-1.5W | No | 
SOT223 | 90 | ~0.5-0.7W | No | 
SOT23 | 200 | ~0.25W | No | 
Or, get your calculator out->

## Slide 32: Calculate thermal limit for TO-220
PDISS,MAX = (TJ,MAX - TAMBIENT,MAX) / (RJA)
PDISS,MAX = (110) / (19) = 5.8W
You need some margin on this. 3-4W might be OK
40°C

## Slide 33: How much does a heat sink help?
PDISS,MAX = (TJ,MAX - TAMBIENT,MAX) / (RJC + RCA)
PDISS,MAX = (110) / (3+13) = 6.9W (compared to 5.8W bare)
~20% improvement, 4-5W
These numbers can be very rough:
Air flow around part/heat sink
Surface mount parts can be highly affected by PCB layout
Rules of thumb:
TO-220 is good for 2-4W of power w/o heat sink, can be improved to 4-5W easily, significantly more requires very large heat sinks and/or fan cooling
SMT is good for 0.25W to 2.5W depending on part, package and PCB layout

## Slide 34: Appendix

## Slide 35: A Quick Battery Primer
Important battery terms:
Voltage, e.g. 1.5V
Voltage range, 0.9 to 1.5V
Capacity, e.g. 500mAh
Discharge rate, e.g. 10C
High current applications - Killswitch
+
Proper schematic for a single cell
+

## Slide 36: Series vs Parallel Batteries
Batteries in series:
Multiply voltage, capacity stays the same
Batteries in parallel:
Multiply capacity, voltage stays the same
+
+
+
Series combination yields
4.5V @ 2800mAh
1.5V 2800mAh
1.5V 2800mAh
1.5V 2800mAh
Parallel combination yields
1.5V @ 8400mAh
+
+
+

## Slide 37: Battery discharge curve This is the primary challenge
Capacity
Chemistry
Discharge rates
1C = 500mA
2C = 1000mA
3C = 1500mA
Rated as “3.6V”

## Slide 38: Battery Chemistry Comparison
http://batteryuniversity.com/learn/article/primary_batteries
Rated: low discharge current
Actual: 1C discharge current

## Slide 39: Battery internal resistance
Remember Ohm’s law:
V = I x R
Battery voltage depends on current
Might matter for higher current circuits
+
1.5V
Load
Ri
Battery model
I

## Slide 40: Powering off of Batteries
Options:
Operate directly off battery if circuit allows
Stack batteries and regulate down to desired voltage
Buck-boost regulator if battery voltage range straddles desired voltage
Low dropout linear regulators (e.g. 0.2V vs 1.0V) can significantly improve battery life
Battery Configuration | Voltage Range
3 alkaline cells | 2.7V to 4.5V
4 alkaline cells | 3.6V to 6.0V
9v cell | 4.8V to 9.0V
3 NiCd cells | 3.3V to 4.2V
NiMH | Similar to alkaline
1 Li+ (Li ion) cell | 2.8V to 4.2V

## Slide 41
LM7805
Thermal Management
First, a Fun Look Inside the LM7805

## Slide 42: LM7805 Die
http://www.righto.com/2014/09/reverse-engineering-counterfeit-7805.html
Capacitor

## Slide 43
LM7805
Thermal Management What are we protecting?
Thermal management is about protecting this from overheating