## Slide 1: Using, Choosing and Abusing Transistors
Ray Crampton, Feb 2019
Add more practical examples

## Slide 3: Two major types of transistors Current controlled & Voltage controlled
Falstad link

## Slide 4: But, voltage drive can be converted into current drive
The resistor effectively changes a voltage drive to a current drive

## Slide 5: Each major type has complementary versions
Falstad link
Falstad link
n-type is low side
p-type is high side

## Slide 6: “Common Emitter/Source” Inverts

## Slide 7: Complementary Bipolar Output
Falstad link

## Slide 8: Complementary MOSFET Output
Falstad link

## Slide 9: BJT Motor or LED Driver Example
Why is a transistor used here?

## Slide 10: BJT Photodiode Example
Why is a transistor used here?

## Slide 11: High voltage motor control
Why is a transistor used here?

## Slide 12: Two transistor oscillator

## Slide 13: If they’re the same, why choose one over the other?
BJTs are generally easier to select and use
but… not always

## Slide 14: MOSFET Examples
Note the “body diode” which is intrinsic to all MOSFETs

## Slide 15: MOSFET, Body Diode Can be Useful
Normal operation is through body diode.
During reverse polarity, FET is off and diode blocks current flow

## Slide 16: Key Bipolar Transistor Specs
Collector-emitter Breakdown Voltage
Maximum operating C-E should be 20-50% lower
Maximum continuous collector current
You should be below this with some margin ~20%
fT – frequency at which gain falls to 1
Should be > 100x your operating frequency
Avoid super high frequency transistors (1GHz!)

## Slide 17: Key MOSFET Specs
Drain-Source Breakdown Voltage
Maximum operating D-S should be 20-50% lower
Gate threshold voltage
You should be well above/below this
On-Voltage (or On-Resistance)
Should be low enough

## Slide 18: MOSFET vs Bipolar Pros/Cons
Bipolar
Easier to drive voltage-wise
Rugged
MOSFET
Can be more efficient
Can switch faster
Gate easier to drive current-wise
Poor selection for 3.3V circuits
Can be difficult to select proper Vt
Very application dependent:
Switching power supplies
Audio Amplifiers
GPIO LED bias
Practical guidance/tendencies:
Low power, low voltage -> bipolar
High current -> FET
High efficiency switching supplies -> FET

## Slide 19: Go-to Transistors
Bipolar – the workhorse for enthusiasts
2N3904 – NPN, 40V, 200mA, 300MHz fT
2N3906 – PNP, -40V. 200mA, 250MHz fT
TIP120 – NPN, 60V, 5A
MOSFETs
Probably don’t want to stock FETs
Wanna play? 2N7000, 2N7002 - NMOS

## Slide 20: Common Bipolar Pinouts

## Slide 21: Typical Breadboard Application

## Slide 22: MOSFET Schematic Symbols
There are many, many variations on these
FETs of the same type (P vs N) behave similar to each other
Be aware but don’t fret over it too much

## Slide 23: Transistors as Amplifiers

## Slide 24: A Linear Amplifier
Falstad Simulation

## Slide 25: Not a good design
Falstad Simulation
Problems
Gain will vary too much with β (hfe) variation
Linearity isn’t very good
Input dynamic range is poor
Circuit needs fine-tuning per transistor used

## Slide 26: A Better Design
Gain ~= -Rc/Re
Improved distortion
Improved dynamic range
Less sensitive to individual transistor characteristics

## Slide 27: Common Configurations
V and I gain
Low input R
Low output R
V gain
Low input R
High output R
I gain
High input R
Low output R

## Slide 28: Darlington Pair
Gain is squared (100 becomes 10,000)

## Slide 29: Differential Pair

## Slide 30: Simple Op-Amp

## Slide 31: Simple Op-Amp Usage
Simple circuit
Near ideal performance