## Slide 1: Advanced Serial Communications
January-2023

## Slide 2: Concepts to Cover
Signal bandwidth
Logic Analyzer vs oscilloscope
High speed serial concepts (PCIe examples)
Advanced I2C
Advanced SPI
Long interconnect (wires)
Error detection
Long wires demo

## Slide 3: What is the bandwidth of a signal?
100kHz
0ns rise time
100kHz
20ns rise time
100kHz
300ns rise time
<---1/100kHz = 10µs--->
<---1/100kHz = 10µs--->
100kHz
Sine wave

## Slide 4: Logic Analyzer vs Oscilloscope

## Slide 5: Eye Diagrams
Not particularly useful for the things we do

## Slide 6: Eye Diagram of Arduino Nano I2C
Normally not very useful!
Persistence
+/- Trigger

## Slide 7: High Speed : “The Channel”
Transmitter
PCB/Wires/
Connectors
Receiver
Receiver
Transmitter
PCB/Wires/
Connectors
Integrated circuit
Integrated circuit

## Slide 8: PCIE Channel
Transmitter
PCB/Wires/
Connectors
Receiver
Receiver
Transmitter
PCB/Wires/
Connectors
Integrated circuit
Integrated circuit

## Slide 9: Signal Integrity

## Slide 10: PCIe 3.0 Equalization
No EQ
Tx EQ
Rx EQ

## Slide 11: Some PHY characteristics
Standard | Data Rate | Signaling Voltage
RS232 | 20kbps | +/-5V to +/-15V
I2C | 100kbps to 3.2Mpbs | 1.2V, 3.3V, 5V
SPI | >40Mbps | 1.2V, 3.3V, 5V
USB1 | 1.5/12Mbps | 0V / 3.3V
USB2 | 480Mbps | +/-400mv, diff
USB3.2 Gen 2x1 | 10Gbps | +/-400mV, diff
USB4 Gen 3x2 | 40Gbps | +/-400mV, diff
The large voltage swings and low speeds of RS232, I2C, SPI make them accessible
The high speeds of USB2-4 and PCIe require very expensive scopes ($3-5k) and logic analyzers (>$1k) and extensive signal integrity experience.

## Slide 12: Takeaways
Architectures are kind of cool
There’s a lot of technology in that simple bus
Interested in playing with your own PCIe or high speed USB hardware?
  Consider buying an FPGA or CPU card with the PHY taken care of

## Slide 13: I2C – Advanced Topics
Multi-master
  Clock synchronization
  Arbitration
Clock stretching
Level translation
Pull-up resistor sizing

## Slide 14: Clock Synchronization
Fastest master sets the high period
Slowest master sets the low period
All controllers monitor SCL to coordinate
Source: TI TIPL6104

## Slide 15: Arbitration
The first controller to send a low bit while the other sends a high bit, wins. The other stops.
Source: TI TIPL6104

## Slide 16: Clock Stretching
Slave can hold SCL low while it does things
Source: https://prodigytechno.com/i2c-clock-stretching/
Note: RPi don’t’ handle SCL stretching well
Not all slaves can stretch (or even have SCL drivers)
Arduino slave: wire.stretchClock(true)

## Slide 17: Level Translation

## Slide 18: Resistor Sizing - ~10pF bus
20kΩ -30kΩ pull-up
10kΩ pull-up
4.7kΩ pull-up
1kΩ pull-up

## Slide 19: Resistor Sizing – 4.7kΩ pull-ups
10pF bus
110pF bus
230pF bus
480pF bus (!!!)

## Slide 20: Pull-Up Resistor Sizing
4.7kΩ is a great general recommendation
Estimate bus capacitance
  10pF per receiver (slave)
  0.5pF / inch of PCB (FR4, 62mil thick, 25mil line width)
  Pair of 20 gauge wires: 1pF / inch + inductive effects
  = = 1.5kΩ
  = = 11.8kΩ

## Slide 21: SPI – Advanced Topics
In some ways, simpler than I2C
  No arbitration (only one master)
  No pull-up resistors
No slave ACK – are you talking to a void?
Long wire issues:
  Line drivers
  Propagation delay
  Clock feedback
  Far-end terminations

## Slide 22
Line drivers
Propagation delay
Clock feedback
Far-end terminations
Source: https://www.ti.com/lit/an/slyt441/slyt441.pdf

## Slide 23: Long Wires
Long interconnect may need attention
  What is “long”?
Can cause a few issues
  Ringing
  Reflections
  Rise time
  Interference

## Slide 24: Ringing

## Slide 25: Ringing
I2C output of a micro through 14’ of wire
~9µH of self inductance (All About Circuits)
  Under-estimates loop inductance!
Assume 25pF capacitance
Fresonant = 1/(2*pi*sqrt(L*C)) = 1/(2*pi*sqrt(9e-6 * 25e-12)) = 10.6MHz
Close estimate to the 7.8MHz we measured
Ringing can be exacerbated by probing technique

## Slide 26: How to fix this?
Reduce I2C pull-up resistor values
Reduce data rate (*** trick question ***)
Shorten wire length
Reduce wire loop size
Add series-R, shunt-C at the end of the line
Clock at source
Clock before RC
Clock after RC
(100Ω/100pF)

## Slide 27: Yeah, this would work
Clock at source
Clock before RC
Clock after RC
(50Ω/47pF)

## Slide 28: Error Detection
  One simple method – CRC-8
01010010 01010111 01111001
01111010
Data (‘Ray’)
CRC-8
01010010 01010111 01111001 01111010
  Not guaranteed – there are only 256 CRC values for all possible data inputs.
  Cannot be done with typical SPI or I2C slaves, this is more useful if you write code on both ends
  For anything other than hobby work – use correction